# How Numbers Are Represented
The nature of MIDI means that data can only use the 7 lower bits of a byte so data is packed into 8 bytes: the first byte contains the MSBs of the following 7 bytes. The least significant bit in the MSB byte corresponds to the last byte in the sequence, the 7th bit corresponds to the first byte in the sequence:
MM 01 02 03 04 05 06 07
|
+- 7 6 5 4 3 2 1 MM bits

After unpacking, when a numeric value is expected, examine the most significant bit of the number. If set the rest of the byte contains the number of bytes following which comprise the number (usually 1 or 2)
The subsequent bytes can then be combined to form the number.
Example 1: single byte, MSB not set
00 – 7F = 0 – 127
Example 2: 2 bytes (80, 81)
81: 80 + 01 indicates byte contains number of bytes (1)
80: Number is in range 80 – FF (128 – 255)
Example 3: 3 bytes (82, 01, 40)
82: 80 + 02 indicates byte contains number of bytes (2)
01: 256 x 1 = 256
40: +64
Number is 256 + 64 = 320
Max number is FFFF