# Patch Change (Code 2D) SysEx Commands
## Message Construct
00 00 10	Manufacturer ID
00	MIDI Channel
56	Device ID
2D	Command code (2D)
00 01
01	Bank (00: Factory, 01: User)
01	Patch number (0 – 2F)
00
XX	Checksum

## Acknowledgement
00 00 10	Manufacturer ID
00	MIDI Channel
56	Device ID
7E	Command code (acknowledged)
00 01 2D 00	Code being acknowledged (2D)
XX	Checksum

# Parameter Change (Code 2C) SysEx Commands
## Message Construct
00 00 10	Manufacturer ID
00	MIDI Channel
56	Device ID
2C	Command code (2C)
00	Packed data MSB
02 00
01	Section
00	Parameter
VV	Value 1, 2 or 3 bytes (see how numbers are represented)
XX	Checksum

## Acknowledgement
00 00 10	Manufacturer ID
00	MIDI Channel
56	Device ID
7E	Command code (acknowledged)
00 01 2C 00	Code being acknowledged (2C)
XX	Checksum

## Sections
CODE	NAME
01	Pickup Simulator
02	Wah
03	Compressor
04	Whammy/IPS
05	Warp
06	Green Amp
07	Green Cabinet
08	Red Amp
09	Red Cabinet
0A	Noise Gate
0B	Chorus/Mod
0C	Delay
0D	Reverb

### Section 01 (Pickup Simulator) Parameters
PARAMETER	NAME	VALUES
00	Type	00: Off / 01: Single Coil>Humb / 02: Humb>Single Coil

### Section 02 (Wah) Parameters
PARAMETER	NAME	VALUES
00	Type	00: Cry, 01: Boutique, 02: Full
01	On/Off	00: Off, 01: On
02	Min	00 – 63 (0 – 99)
03	Max	00 – 63 (0 – 99)
04	Pedal	00 – 63 (0 – 99)

### Section 03 (Compressor) Parameters
PARAMETER	NAME	VALUES
00
01	On/Off	00: Off, 01: On
02	Attack	00: Fast, 01: Medium, 02: Slow
03	Ratio	00: 1.2:1 01: 1.5:1 02: 1.8:1 03: 2.0:1 / 04: 2.5:1 05: 3.0:1 06: 4.0:1 07: 5.0:1 / 08: 8.0:1 09: 10:1 0A: 20:1 0B: Inf
04	Threshold	00 – 63 (0 – 99)
05	Gain	00 – 14 (0 – 20)

### Section 04 (Whammy/IPS) Parameters
#### Type 00: Whammy
PARAMETER	NAME	VALUES
00	Type *	00: Whammy
01	On/Off	00: Off, 01: On
02	Shift	00: 1 Oct Up 01: 2 Oct Up / 02: 2nd Down 03: 2nd Dn Rev / 04: 4th Down 05: 1 Oct Dn / 06: 2 Oct Dn 07: Dive Bomb / 08: m3>Maj3 Up 09: 2nd>Maj3 Up / 0A: 3rd>4th Up 0B: 4th>5th Up / 0C: 5th>Oct Up 0D: Harm Oct Up / 0E: Harm Oct Dn 0F: Oct Up>Dn
03	Pedal	0 – 63 (0 – 99)
04	Mix	00 – 63 (0 – 99)

#### Type 01: IPS
PARAMETER	NAME	VALUES
00	Type *	01: IPS
01	On/Off	00: Off, 01: On
02	Shift	00: Oct Down 01: 7th Down / 02: 6th Down 03: 5th Down / 04: 4th Down 05: 3rd Down / 06: 2nd Down 07: 2nd Up / 08: 3rd Up 09: 4th Up / 0A: 5th Up 0B: 6th Up / 0C: 7th Up 0D: Oct Up
03	Scale	00: Major 01: Minor / 02: Dorian 03: Mixolydian / 04: Lydian 05: Harm Minor
04	Key	00: E 01: F 02: Gb 03: G / 04: Ab 05: A 06: Bb 07: B / 08: C 09: Db 0A: D 0B: Eb
05	Level	00 – 63 (0 – 99)

#### Type 02: Detune
PARAMETER	NAME	VALUES
00	Type *	02: Detune
01	On/Off	00: Off, 01: On
02	Shift	00 / 0C / 18 (-24 / 0 / 24) (Step 2)
03	Level	00 – 63 (0 – 99)

#### Type 03: Pitch
PARAMETER	NAME	VALUES
00	Type *	03: Pitch
01	On/Off	00: Off, 01: On
02	Shift	00 / 18 / 30 (-24 / 0 / 24) (Step 1)
03	Level	00 – 63 (0 – 99)

* Type change causes GENX1 to transmit associated parameters
### Section 05 (Warp) Parameters
PARAMETER	NAME	VALUES
00
01	Amp Select	00: Green, 01: Red, 02: Yellow
02	Amp	00 – 62 (1 – 99) Green → Red
03	Cabinet	00 – 62 (1 – 99) Green → Red
04

### Section 06 (Green Amp) Parameters
PARAMETER	NAME	VALUES
00	Amp Type *	00: Direct 01: Blkfac / 02: Boutiq 03: Rectif / 04: Hotrod 05: Tweed / 06: Brtcmb 07: Clntub / 08: Brtstk 09: Crunch / 0A: Higain 0B: Blues / 0C: Modgan 0D: Fuzz / 0E: Bassmn 0F: Hiwatg / 10: Acoust 11: User 1 / 12: User 2 13: User 3 / 14: User 4 15: User 5 / 16: User 6 17: User 7 / 18: User 8 19: User 9 / 1A: Custom
01	Gain	00 – 63 (0 – 99)
02	Bass Freq	00 – FA (50Hz – 300Hz) Step 1Hz **
03	Bass Level	00/0C/18 (-12/0/+12)
04	Mid Frequency	00 – 125C (300Hz – 5KHz) Step 1 Hz
05	Mid Level	00/0C/18 (-12/0/+12)
06	Treble Freq	00 – 1D4C (500Hz – 8KHz) Step 1Hz
07	Treble Level	00/0C/18 (-12/0/+12)
08	Level	00 – 63 (0 – 99)

* selecting amp type causes additional parameters to be transmitted
** 1 or 2 bytes (see FLAGS byte in message construct)
### Section 07 (Green Cabinet) Parameters
PARAMETER	NAME	VALUES
00	Cabinet Type *	00: Direct 01: Am2x12 / 02: Br4x12 03: V 4x12 / 04: Br2x12 05: Am1x12 / 06: Bl2x12 07: Fn4x12 / 08: Gr4x12 09: User 1 / 0A: User 2 0B: User 3 / 0C: User 4 0D: User 5 / 0E: User 6 0F: User 7 / 10: User 8 11: User 9 / 12: Custom
01	Tuning	00/18/30 (-12/0/+12 in 0.5 steps)

### Section 08 (Red Amp) Parameters
PARAMETER	NAME	VALUES
00	Amp Type *	00: Direct 01: Blkfac / 02: Boutiq 03: Rectif / 04: Hotrod 05: Tweed / 06: Brtcmb 07: Clntub / 08: Brtstk 09: Crunch / 0A: Higain 0B: Blues / 0C: Modgan 0D: Fuzz / 0E: Bassmn 0F: Hiwatg / 10: Acoust 11: User 1 / 12: User 2 13: User 3 / 14: User 4 15: User 5 / 16: User 6 17: User 7 / 18: User 8 19: User 9 / 1A: Custom
01	Gain	00 – 63 (0 – 99)
02	Bass Freq	00 – FA (50Hz – 300Hz) Step 1Hz **
03	Bass Level	00/0C/18 (-12/0/+12)
04	Mid Frequency	00 – 125C (300Hz – 5KHz) Step 1 Hz
05	Mid Level	00/0C/18 (-12/0/+12)
06	Treble Freq	00 – 1D4C (500Hz – 8KHz) Step 1Hz
07	Treble Level	00/0C/18 (-12/0/+12)
08	Level	00 – 63 (0 – 99)

* selecting amp type causes additional parameters to be transmitted
** 1 or 2 bytes (see FLAGS byte in message construct)
### Section 09 (Red Cabinet) Parameters
PARAMETER	NAME	VALUES
00	Cabinet Type *	00: Direct 01: Am2x12 / 02: Br4x12 03: V 4x12 / 04: Br2x12 05: Am1x12 / 06: Bl2x12 07: Fn4x12 / 08: Gr4x12 09: User 1 / 0A: User 2 0B: User 3 / 0C: User 4 0D: User 5 / 0E: User 6 0F: User 7 / 10: User 8 11: User 9 / 12: Custom
01	Tuning	00/18/30 (-12/0/+12 in 0.5 steps)

### Section 0A (Noise Gate) Parameters
#### Type 00: Silencer
PARAMETER	NAME	VALUES
00	Type *	00: Silencer
01	On/Off	00: Off, 01: On
02	Threshold	00 – 28 (0 – 40)
03	Attack	00 – 09 (0 – 9)

#### Type 01: Pluck
PARAMETER	NAME	VALUES
00	Type *	01: Pluck
01	On/Off	00: Off, 01: On
02	Threshold	00 – 28 (0 – 40)
03	Attack	00 – 09 (0 – 9)
04	Sensitivity	00 – 63 (0 – 99)

* Type change causes GENX1 to transmit associated parameters
### Section 0B (Chorus/Mod) Parameters
#### Type 00: Chorus
PARAMETER	NAME	VALUES
00	Type *	00: Chorus
01	On/Off	00: Off, 01: On
02	Chorus	00 – 62 (1 – 99)
03	Depth	00 – 62 (1 – 99)
04	Pre Delay	00 – 13 (1 – 20)
05	Waveform	00: Triangle, 01: Sine, 02: Square
06	Balance	00 – 63 – C6 (-99 – 0 – 99) **
07	Mix	00 – 63 (0 – 99)

#### Type 01: Flanger
PARAMETER	NAME	VALUES
00	Type *	01: Flanger
01	On/Off	00: Off, 01: On
02	Speed	00 – 62 (1 – 99)
03	Depth	00 – 62 (1 – 99)
04	Regen	00 – 63 (0 – 99)
05	Waveform	00: Triangle, 01: Sine, 02: Square
06	Balance	00 – 63 – C6 (-99 – 0 – 99) **
07	Mix	00 – 63 (0 – 99)

#### Type 02: Phaser
PARAMETER	NAME	VALUES
00	Type *	02: Phaser
01	On/Off	00: Off, 01: On
02	Phaser/Speed	00 – 62 (1 – 99)
03	Phaser/Depth	00 – 62 (1 – 99)
04	Phaser/Regen	00 – 63 (0 – 99)
05	Phaser/Waveform	00: Triangle, 01: Sine, 02: Square
06	Phaser/Balance	00 – 63 – C6 (-99 – 0 – 99) **
07	Phaser/Mix	00 – 63 (0 – 99)

#### Type 03: Triggered Flanger
PARAMETER	NAME	VALUES
00	Type *	03: Triggered Flanger
01	On/Off	00: Off, 01: On
02	Speed	00 – 62 (1 – 99)
03	Sensitivity	00 – 62 (1 – 99)
04	LFO Start	00 – 63 (0 – 99)
05	Mix	00 – 63 (0 – 99)

#### Type 04: Triggered Phaser
PARAMETER	NAME	VALUES
00	Type *	04: Triggered Phaser
01	On/Off	00: Off, 01: On
02	Speed	00 – 62 (1 – 99)
03	Sensitivity	00 – 62 (1 – 99)
04	LFO Start	00 – 63 (0 – 99)
05	Mix	00 – 63 (0 – 99)

#### Type 05: Tremelo
PARAMETER	NAME	VALUES
00	Type *	05: Tremelo
01	On/Off	00: Off, 01: On
02	Speed	00 – 62 (1 – 99)
03	Depth	00 – 63 (0 – 99)
04	Waveform	00: Triangle, 01: Sine, 02: Square

#### Type 06: Panner
PARAMETER	NAME	VALUES
00	Type *	06: Panner
01	On/Off	00: Off, 01: On
02	Speed	00 – 62 (1 – 99)
03	Depth	00 – 63 (0 – 99)
04	Waveform	00: Triangle, 01: Sine, 02: Square

#### Type 07: Vibrato
PARAMETER	NAME	VALUES
00	Type *	07: Vibrato
01	On/Off	00: Off, 01: On
02	Speed	00 – 62 (1 – 99)
03	Depth	00 – 62 (1 – 99)
04	Waveform	00: Triangle, 01: Sine, 02: Square

#### Type 08: Rotary Speaker
PARAMETER	NAME	VALUES
00	Type *	08: Rotary Speaker
01	On/Off	00: Off, 01: On
02	Speed	00 – 63 (0 – 99)
03	Depth	00 – 63 (0 – 99)
04	Doppler	00 – 63 (0 – 99)
05	X-Over Freq	00 – 82 (200Hz – 1.50kHz) ** / Step 10Hz
06	Balance	00 – 63 – C6 (-99 – 0 – 99) **
07	Mix	00 – 63 (0 – 99)

#### Type 09: Auto Yah
PARAMETER	NAME	VALUES
00	Type *	09: Auto Yah
01	On/Off	00: Off, 01: On
02	Speed	00 – 62 (1 – 99)
03	Depth	00 – 62 (1 – 99)
04	Range	00 – 31 (0 – 50)
05	Balance	00 – 63 – C6 (-99 – 0 – 99) **
06	Mix	00 – 63 (0 – 99)

#### Type 0A: YaYa
PARAMETER	NAME	VALUES
00	Type *	0A: YaYa
01	On/Off	00: Off, 01: On
02	Pedal	00 – 63 (0 – 99)
03	Depth	00 – 62 (1 – 99)
04	Range	00 – 31 (0 – 50)
05	Balance	00 – 63 – C6 (-99 – 0 – 99) **
06	Mix	00 – 63 (0 – 99)

#### Type 0B: Synthtalk
PARAMETER	NAME	VALUES
00	Type *	0B: Synthtalk
01	On/Off	00: Off, 01: On
02	Attack	00 – 63 (0 – 99)
03	Release	00 – 63 (1 – 100)
04	Vox	00 – 63 (0 – 99)
05	Balance	00 – 63 – C6 (-99 – 0 – 99) **
06	Delay	00 – 62 (1 – 99)

#### Type 0C: Envelope
PARAMETER	NAME	VALUES
00	Type *	0C: Envelope
01	On/Off	00: Off, 01: On
02	Sensitivity	00 – 62 (1 – 99)
03	Range	00 – 62 (1 – 99)
04	Balance	00 – 63 – C6 (-99 – 0 – 99) **
05	Mix	00 – 63 (0 – 99)

#### Type 0D: Detune
PARAMETER	NAME	VALUES
00	Type *	0D: Detune
01	On/Off	00: Off, 01: On
02	Shift Amount	00/18/30 (-24/0/+24) (Step 1)
03	Balance	00 – 63 – C6 (-99 – 0 – 99) **
04	Mix	00 – 63 (0 – 99)

#### Type 0E: Pitch
PARAMETER	NAME	VALUES
00	Type *	0E: Pitch
01	On/Off	00: Off, 01: On
02	Shift Amount	00/0C/24 (-12/0/+24) (Step 1)
03	Balance	00 – 63 – C6 (-99 – 0 – 99) **
04	Level	00 – 63 (0 – 99)

* Type change causes GENX1 to transmit associated parameters
** 1 or 2 bytes (see FLAGS byte in message construct)
`
### Section 0C (Delay) Parameters
PARAMETER	NAME	VALUES
00	Type *	00: Mono 01: Ping Pong / 02: Analog 03: Alg Pong
01	On/Off	00: Off, 01: On
02	Delay Time	00 – 7D0 (0ms – 2s) Step 1ms ***
03	Feedback	00 – 64 (0 – 99 + R-Hold)
04	Duck Thresh	00 – 63 (1 – 99 + Off)
05	Duck Atten	00 – 63 (0 – 99)
06	Balance	00 – 63 – C6 (-99 – 0 – 99) **
07	Level	00 – 63 (0 – 99)

* Type change causes GENX1 to transmit associated parameters
** 1 or 2 bytes (see FLAGS byte in message construct)
*** 1, 2 or 3 bytes (see FLAGS byte in message construct)
### Section 0D (Reverb) Parameters
PARAMETER	NAME	VALUES
00	Type *	00: Studio 01: Room / 02: Club 03: Plate / 04: Hall 05: Amphitheatre / 06:9 Church 07: Garage / 08: Arena 09: Spring
01	On/Off	00: Off, 01: On
02	Pre Delay	00 – 0F (0 – 15)
03	Decay	00 – 62 (1 – 99)
04	Damping	00 – 64 (0 – 99)
05	Balance	00 – 63 – C6 (-99 – 0 – 99) **
06	Level	00 – 63 (0 – 99)

* Type change causes GENX1 to transmit associated parameters
** 1 or 2 bytes (see FLAGS byte in message construct)
### Section 8A (LFO 1) Parameters
PARAMETER	NAME	VALUES
TBC	Speed	00 – B9 / (0.05Hz – 0.99Hz) Step 0.01Hz / (1Hz – 10Hz) Step 0.1Hz
TBC	Waveform	00: Triangle, 01: Sine, 02: Square

### Section 8B (LFO 2) Parameters
PARAMETER	NAME	VALUES
TBC	Speed	00 – B9 / (0.05Hz – 0.99Hz) Step 0.01Hz / (1Hz – 10Hz) Step 0.1Hz
TBC	Waveform	00: Triangle, 01: Sine, 02: Square

# Expression Assign (Code 26) SysEx Commands
## Message Construct
Bytes are packed with first byte containing MSBs of the following 7 bytes (packed) for 5 parameters, each followed by 2 values
00 00 10	Manufacturer ID
00	MIDI Channel
56	Device ID
26	Command code (26)
04 02 02 00 03 00 00 03	Header (packed)
MSB	MSBs
01	Byte 01
02
03
04
05
06
07	Byte 07
…	etc

#### Parameter Packets
SS	Parameter section vector
PP	Parameter value vector
NN	Expression 1 Parameter 1 (Max)
NN	Expression 1 Parameter 1 (Min)
NN (LFO Only)

#### Expression Assign Parameters
Expression 1
Expression 2
Expression 3
LFO 1
LFO 2	8B 02 followed by Speed, Waveform, Linked Parameter, 01, (SS PP), Max, Min

For OFF: SS = 0xFF, PP can be 0xFF or 0x00
## Expression Assign Linked Parameter Values (SS PP)

FF FF	No Link
03 02	Compressor Attack
03 03	Compressor Ratio
03 04	Compressor Threshold
03 05	Compressor Gain
04 02	IPS/Whammy Shift Amount
04 03	IPS/Whammy Pedal
04 04	IPS/Whammy Mix
05 01	Amp Channel
05 02	Amp Warp
05 03	Cab Warp
05 04	Warp
06 01	Green Amp Gain
06 08	Green Amp Level
08 01	Red Amp Gain
08 08	Red Amp Level
0A 02	Gate Threshold
0A 03	Gate Attack
0B 02	Modulation Speed
0B 03	Modulation Depth
0B 04	Modulation Regeneration
0B 06	Modulation Balance
0B 07	Modulation Mix
0C 03	Delay feedback
0C 04	Delay Duck Threshold
0C 05	Delay Duck Attenuation
0C 06	Delay Balance
0C 07	Delay Level
0D 02	Reverb Pre Delay
0D 03	Reverb Decay
0D 05	Reverb Balance
0D 06	Reverb Level
0E 01	Vol Pre
0E 02	Vol Post
0E 04	LFO1 Speed
0E 05	LFO2 Speed
8A 02	LFO1 parameters follow: Speed, Waveform, Linked Parameter, 01, (SS PP), Max, Min
8V 02	LFO2 parameters follow Speed, Waveform, Linked Parameter, 01, (SS PP), Max, Min

# Patch Name Change (Code 2E) SysEx Commands
## Message Construct
00 00 10	Manufacturer ID
00	MIDI Channel
56	Device ID
2E	Command code (2E)
..	Packed data
XX	Checksum

## Acknowledgement
00 00 10	Manufacturer ID
00	MIDI Channel
56	Device ID
7E	Command code (acknowledged)
00 01 2C 00	Code being acknowledged (2C)
XX	Checksum

## Data Format
01
BB PP	BB: Bank (0 = Factory, 1 = User), PP: Patch (0 – 2F)
BB PP	BB: Bank (0 = Factory, 1 = User), PP: Patch (0 – 2F)
48 59 42 52 49 44	ASCII Name
00 FF	Terminator

Note: Factory names can not be edited