# Packed Data Format

Data is packed in 8 byte “packets”, with the MS bit stripped from 7 parameter bytes, and packed into an eighth byte, which is sent at the start of the 8 byte packet.

Example:

MM 01 02 03 04 05 06 07
|
+- 7 6 5 4 3 2 1 MM bits
# Checksum Error
The following is returned from GENX1 when an incorrect checksum byte is sent in response to a command 08
System Exclusive	F0
Manufacturer ID	00 00 10
Midi Channel	00
Device ID	56
Command Code	7F
Message	00 01 07 08 Command
Checksum	11
End of System Exclusive	F7

# Device Inquiry
System Exclusive	F0
Manufacturer ID	00 00 10
Non Realtime	7E
Midi Channel	7F (All channels)
Inquiry Message/Request	01 00 01 00 00
Checksum	11
End of System Exclusive	F7

## Response (GENX1 MIDI Channel 0)
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Response	00 01 00 56 (??, response, channel, device type)
Checksum	13
End of System Exclusive	F7

## Response (GENX1 MIDI Channel 1)
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	01
Device ID	56
Response	00 01 01 56 (??, response, channel, device type)
Checksum	13
End of System Exclusive	F7

# Device Connected
Transmitted by GENX1 when powered on
System Exclusive	F0
Manufacturer ID	00 00 10
Non Realtime	7E
Midi Channel	7F (All channels)
Message	02 00 01 00
Device ID	56
Checksum	44
End of System Exclusive	F7

# Get Current Patch
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	76 20 01
Checksum	6E
End of System Exclusive	F7

## Response
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	2D
	00 01
Bank	00: Factory, 01: User
Patch	00: 0 - 2F
Pad	00
Checksum	XX
End of System Exclusive	F7

# Command 70
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	70
Data	00 01 08
Checksum	3F
End of System Exclusive	F7

## Response Acknowledge Code 7E
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	7E
Data	00 01
Response Code	70 00
Checksum	XX
End of System Exclusive	F7

# Status Request 05
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	05
Data	00 01
Checksum	42
End of System Exclusive	F7

## Response Data 06
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	06
Data	00 15 00 25
UnPacked Data	01 00 6F 00 15 00 25 30 / 30 03 01 05 01 01 02 01 / 05 01 06 01 07 01 08 02 / 09 01 0A 02 0B 01 0C 01 / 0D 01 0E 01 0F 01 10 01 / 11 01 12 01 13 01 14 01 / 15 01 20 01 21 01 22 01 / 23 01 24 02 25 01 26 02 / 27 01 28 01 29 01 2A 01 / 2B 01 2C 02 2D 01 2E 01 / 70 01 71 01 72 01 73 01 / 74 01 75 01 76 01 7E 01 / 7F 01	Current Patch: / 01: User, 00: Factory / 0-2F: Patch 1 - 128
Checksum	41
End of System Exclusive	F7

# Status Request 07 (Subcode 00)
Returns enumerated Amp and Cabinet null terminated/padded names.
Note that basic and user amp/cab names are sent using similar packets. Check if these can be specified in the 07 command.
Highlighted 3C 11 11 indicates 17 amp names follow. 3D 09 09 indicates 9 cabinet names follow.
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	07
Data	00 01
Subcode	XX 00: Basic, 01: User
Checksum	40
End of System Exclusive	F7

## Response Data 08
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	08
	: 0 = basic, 1 = user / : number of names / : 3C = amp names, 3D = cab names
Packed/Unpacked Data	00 02 00 02 3C 11 11 00 / 00 44 49 52 45 43 54 00 / 00 01 42 4C 4B 46 41 43 / 00 00 02 42 4F 55 54 49 / 00 51 00 03 52 45 43 54 / 00 49 46 00 04 48 4F 54 / 00 52 4F 44 00 05 54 57 / 00 45 45 44 20 00 06 42 / 00 52 54 43 4D 42 00 07 / 00 43 4C 4E 54 55 42 00 / 00 08 42 52 54 53 54 4B / 00 00 09 43 52 55 4E 43 / 00 48 00 0A 48 49 47 41 / 00 49 4E 00 0B 42 4C 55 / 00 45 53 20 00 0C 4D 4F / 00 44 47 41 4E 00 0D 46 / 00 55 5A 5A 20 20 00 0E / 00 42 41 53 53 4D 4E 00 / 00 0F 48 49 57 41 54 47 / 00 00 10 41 43 4F 55 53 / 00 54 00 3D 09 09 00 44 / 00 49 52 45 43 54 00 01 / 00 41 4D 32 58 31 32 00 / 00 02 42 52 34 58 31 32 / 00 00 03 56 20 34 58 31 / 00 32 00 04 42 52 32 58 / 00 31 32 00 05 41 4D 31 / 00 58 31 32 00 06 42 4C / 00 32 58 31 32 00 07 46 / 00 4E 34 58 31 32 00 08 / 00 47 52 34 58 31 32 00	02 00 02 3C 11 11 00 44 . . . < . . . D / 49 52 45 43 54 00 01 42 I R E C T . . B / 4C 4B 46 41 43 00 02 42 L K F A C . . B / 4F 55 54 49 51 00 03 52 O U T I Q . . R / 45 43 54 49 46 00 04 48 E C T I F . . H / 4F 54 52 4F 44 00 05 54 O T R O D . . T / 57 45 45 44 20 00 06 42 W E E D . . B / 52 54 43 4D 42 00 07 43 R T C M B . . C / 4C 4E 54 55 42 00 08 42 L N T U B . . B / 52 54 53 54 4B 00 09 43 R T S T K . . C / 52 55 4E 43 48 00 0A 48 R U N C H . . H / 49 47 41 49 4E 00 0B 42 I G A I N . . B / 4C 55 45 53 20 00 0C 4D L U E S . . M / 4F 44 47 41 4E 00 0D 46 O D G A N . . F / 55 5A 5A 20 20 00 0E 42 U Z Z . . B / 41 53 53 4D 4E 00 0F 48 A S S M N . . H / 49 57 41 54 47 00 10 41 I W A T G . . A / 43 4F 55 53 54 00 3D 09 C O U S T . = . / 09 00 44 49 52 45 43 54 . . D I R E C T / 00 01 41 4D 32 58 31 32 . . A M 2 X 1 2 / 00 02 42 52 34 58 31 32 . . B R 4 X 1 2 / 00 03 56 20 34 58 31 32 . . V 4 X 1 2 / 00 04 42 52 32 58 31 32 . . B R 2 X 1 2 / 00 05 41 4D 31 58 31 32 . . A M 1 X 1 2 / 00 06 42 4C 32 58 31 32 . . B L 2 X 1 2 / 00 07 46 4E 34 58 31 32 . . F N 4 X 1 2 / 00 08 47 52 34 58 31 32 . . G R 4 X 1 2 / 00 .
Checksum	2E
End of System Exclusive	F7

# Status Request 07 (Subcode 01, 02, 03)
Commands appear to be unrecognised or malformed
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	07
Data	00 01
Subcode	CC
Checksum	CX
End of System Exclusive	F7

## Response Data 08
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	08
Data	00 02
Subcode	CC
Data	02 3C 09 00 3D 00 09 00
Checksum	CX
End of System Exclusive	F7

# Get User Patch Names (12)
Returns enumerated user patch names null terminated from data + 2. 01 30 may indicate user/48 names
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	12
Data	00 01 01 00
Checksum	54
End of System Exclusive	F7

## Response Data 13
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	13
Packed/Unpacked Data	00 01 30 48 59 42 52 49 / 00 44 00 43 4C 4E 43 48 / 00 4F 00 32 43 48 55 4E / 00 4B 00 57 41 52 50 4D / 00 45 00 42 4C 4B 42 41 / 00 53 00 4D 45 41 54 58 / 00 32 00 45 52 49 43 20 / 00 4A 00 43 41 52 4C 4F / 00 53 00 4B 4F 42 42 20 / 00 20 00 42 41 53 53 4D / 00 4E 00 4D 41 54 43 48 / 00 44 00 56 4F 58 54 4F / 00 50 00 42 4C 55 44 4C / 00 59 00 42 4C 55 42 41 / 00 4C 00 54 45 58 42 4C / 00 55 00 50 49 43 4B 45 / 00 4E 00 50 53 54 45 45 / 00 4C 00 41 20 4D 49 58 / 00 4F 00 4D 4F 20 57 41 / 00 48 00 46 41 5A 4F 55 / 00 54 00 54 48 49 43 4B / 00 52 00 41 43 4F 55 53 / 00 54 00 43 4D 50 43 4C / 00 4E 00 57 52 4D 43 4C / 00 4E 00 52 45 43 54 46 / 00 59 00 53 4F 4C 4F 20 / 00 20 00 57 48 41 4D 4D / 00 59 00 53 54 41 43 4B / 00 44 00 56 4F 4C 53 57 / 00 4C 00 42 49 47 44 55 / 00 4B 00 4A 41 5A 5A 59 / 00 20 00 35 54 48 53 20 / 00 20 00 46 55 53 4F 4C / 00 4F 00 53 55 52 46 49 / 00 4E 00 46 55 5A 5A 4F / 00 20 00 54 52 45 4D 42 / 00 4F 00 43 4C 4E 57 41 / 00 48 00 46 4E 4B 50 48 / 00 53 00 45 4E 56 4C 4F / 00 50 00 42 4C 4B 46 55 / 00 5A 00 54 55 4E 43 41 / 00 42 00 54 52 47 50 48 / 00 53 00 50 53 59 4E 54 / 00 48 00 52 4F 54 41 52 / 00 59 00 59 41 59 41 20 / 00 20 00 53 54 55 54 54 / 00 52 00 54 52 49 50 4C / 00 54 00 44 49 56 42 4F / 00 4D 00	01 30 48 59 42 52 49 44 . 0 H Y B R I D / 00 43 4C 4E 43 48 4F 00 . C L N C H O . / 32 43 48 55 4E 4B 00 57 2 C H U N K . W / 41 52 50 4D 45 00 42 4C A R P M E . B L / 4B 42 41 53 00 4D 45 41 K B A S . M E A / 54 58 32 00 45 52 49 43 T X 2 . E R I C / 20 4A 00 43 41 52 4C 4F J . C A R L O / 53 00 4B 4F 42 42 20 20 S . K O B B / 00 42 41 53 53 4D 4E 00 . B A S S M N . / 4D 41 54 43 48 44 00 56 M A T C H D . V / 4F 58 54 4F 50 00 42 4C O X T O P . B L / 55 44 4C 59 00 42 4C 55 U D L Y . B L U / 42 41 4C 00 54 45 58 42 B A L . T E X B / 4C 55 00 50 49 43 4B 45 L U . P I C K E / 4E 00 50 53 54 45 45 4C N . P S T E E L / 00 41 20 4D 49 58 4F 00 . A M I X O . / 4D 4F 20 57 41 48 00 46 M O W A H . F / 41 5A 4F 55 54 00 54 48 A Z O U T . T H / 49 43 4B 52 00 41 43 4F I C K R . A C O / 55 53 54 00 43 4D 50 43 U S T . C M P C / 4C 4E 00 57 52 4D 43 4C L N . W R M C L / 4E 00 52 45 43 54 46 59 N . R E C T F Y / 00 53 4F 4C 4F 20 20 00 . S O L O . / 57 48 41 4D 4D 59 00 53 W H A M M Y . S / 54 41 43 4B 44 00 56 4F T A C K D . V O / 4C 53 57 4C 00 42 49 47 L S W L . B I G / 44 55 4B 00 4A 41 5A 5A D U K . J A Z Z / 59 20 00 35 54 48 53 20 Y . 5 T H S / 20 00 46 55 53 4F 4C 4F . F U S O L O / 00 53 55 52 46 49 4E 00 . S U R F I N . / 46 55 5A 5A 4F 20 00 54 F U Z Z O . T / 52 45 4D 42 4F 00 43 4C R E M B O . C L / 4E 57 41 48 00 46 4E 4B N W A H . F N K / 50 48 53 00 45 4E 56 4C P H S . E N V L / 4F 50 00 42 4C 4B 46 55 O P . B L K F U / 5A 00 54 55 4E 43 41 42 Z . T U N C A B / 00 54 52 47 50 48 53 00 . T R G P H S . / 50 53 59 4E 54 48 00 52 P S Y N T H . R / 4F 54 41 52 59 00 59 41 O T A R Y . Y A / 59 41 20 20 00 53 54 55 Y A . S T U / 54 54 52 00 54 52 49 50 T T R . T R I P / 4C 54 00 44 49 56 42 4F L T . D I V B O / 4D 00 00 M . .
Checksum	6D
End of System Exclusive	F7

# Request Current Patch Name (20)
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	20
Data	00 01 02 00 1F
Checksum	7A
End of System Exclusive	F7

## Response Data 21
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	21
Packed Data	00 01 02 00 48 59 42 52 / 09 49 44 00 7F 08 09 29 / 00 00	01 02 00 48 59 42 52 49 . . . H Y B R I / 44 00 FF 08 09 A9 00 D . . . . . .
Checksum	36
End of System Exclusive	F7

Acknowledge message triggers further data dump 8 messages (following pages)
No acknowledgement triggers BADACK message on GNX1

# Acknowledge Patch Dump

System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	7E
Data	00 01 21
Checksum	18
End of System Exclusive	F7

## Patch Dump Reply Message 1 (24)
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	24
Packed Data	00 02 02 00 10 00 00 00 / 02 00 00 50 01 01 10 01 / 04 00 51 02 01 43 05 00 / 00 00 00 63 52 52 03 01 / 40 74 06 00 00 00 07 1C / 04 09 53 04 03 04 05 00 / 00 00 00 00 63 28 05 00 / 40 48 05 00 00 31 01 31 / 00 3C 06 01 2C 09 0A 46 / 15 64 0C 02 08 18 0C 02 / 20 11 14 0C 43 3D 07 01 / 00 5E 02 03 18 3C 08 01 / 01 2C 09 0A 46 64 0C 02 / 2A 08 18 0D 02 11 14 0C / 00 46 3D 09 01 5E 02 03 / 00 06 54 0A 02 26 04 00 / 00 01 0F 00 55 0B 04 6A / 00 05 0D 00 0E 63 3C 56 / 01 0C 02 58 08 03 00 02 / 20 01 4C 19 63 4B 63 1E / 08 57 0D 02 3D 07 04 01 / 00 0A 32 32 63 14 14 0E / 00 00 64 06 00 63 63 03 / 00 00 00 02 0F 00 02 00	02 02 00 10 00 00 00 00 . . . . . . . . / 00 50 01 01 90 01 00 51 . P . . . . . Q / 02 01 C3 05 00 00 00 63 . . . . . . . c / 52 52 03 01 F4 06 00 00 R R . . . . . . / 00 07 1C 09 53 04 03 84 . . . . S . . . / 05 00 00 00 00 63 28 05 . . . . . c ( . / 00 C8 05 00 00 31 01 31 . . . . . 1 . 1 / 3C 06 01 2C 09 0A 46 64 < . . , . . F d / 0C 82 08 98 0C 82 11 94 . . . . . . . . / 0C 43 3D 07 01 5E 02 03 . C = . . ^ . . / 18 3C 08 01 2C 09 0A 46 . < . . , . . F / 64 0C 82 08 98 0D 82 11 d . . . . . . . / 94 0C 46 3D 09 01 5E 02 . . F = . . ^ . / 03 06 54 0A 02 26 04 00 . . T . . & . . / 01 0F 00 55 0B 04 6A 05 . . . U . . j . / 0D 00 0E 63 3C 56 0C 02 . . . c < V . . / 58 08 03 00 82 01 CC 19 X . . . . . . . / 63 4B 63 1E 57 0D 02 BD c K c . W . . . / 07 04 01 0A 32 32 63 14 . . . . 2 2 c . / 14 0E 00 64 06 00 63 63 . . . d . . c c / 03 00 00 02 0F 00 02 00 . . . . . . . .
Checksum	21
End of System Exclusive	F7

## Patch Dump Reply Message 2 (2A)
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	2A
Packed Data	00 01 02 00 3C 06 00 00 / 00 48 49 47 41 49 4E 00 / 1C 02 4B 7E 7F 7F 1C 00 / 05 00 00 00 00 32 13 70 / 70 7F 7F 7F 16 00 00 33 / 17 00 00 4C 13 70 7E 7F / 40 7F 10 00 00 59 00 00 / 1E 14 14 70 7F 7F 7F 0A / 00 00 00 74 00 00 7C 14 / 78 70 7E 7F 7F 04 00 00 / 4B 02 00 00 78 14 70 7E / 7E 7F 7F 7E 7F 7F 04 00 / 0F 00 7D 15 70 7F 7F 7F / 71 78 7F 7F 7A 00 00 7E / 3F 15 70 7E 7F 7F 73 7F / 41 7F 64 00 00 6F 16 70 / 0E 00 00 00 6A 7F 7F 40 / 17 00 00 42 16 70 75 7F / 78 7F 6C 7F 7F 15 00 00 / 51 6C 16 70 21 00 00 4A / 7E 7F 7F 4B 7F 7F 63 16 / 58 70 7B 7F 7F 2C 00 00 / 7B 40 7F 7F 17 16 70 67 / 1F 01 00 1D 7E 7F 09 7E / 6F 7F 7E 15 70 5B 78 7F / 00 53 04 00 78 01 00 0B / 3B 15 70 29 4D 02 63 6E / 7D 7F 30 74 7F 32 13 70 / 78 46 27 7C 5E 57 08 6F / 1D 3B 08 6D 44 72 42 13 / 4A 7E 2F 4F 7E 7B 62 0E / 05 00 00 00 1F 50 01 75 / 33 08 7A 1E 3A 07 6C 44 / 01 0B 1B 30 00 51 79 7F / 6C 63 3C 00 1D 58 0E 4F / 72 75 7F 24 09 00 58 3F / 20 00 6D 3E 0F 44 05 00 / 71 12 69 7F 0E 33 00 3A / 01 7D 0F 3B 00 00 5F 79 / 66 7F 7D 15 00 1D 1F 0F / 06 68 04 00 12 7A 7F 6D / 0B 09 00 34 2F 0F 3F 78 / 44 7F 4A 07 00 49 0A 00 / 29 1B 37 0F 5C 08 00 06 / 73 71 7F 19 03 00 6D 41 / 18 0F 26 7B 7F 19 0C 00 / 0C 38 01 00 68 3F 0F 30 / 1E 01 00 0C 7D 7F 5D 0A / 17 00 60 48 0F 0C 7F 7F / 09 1E 01 00 07 09 00 7A / 43 51 0F 16 00 00 41 7F / 42 7F 66 0A 00 2B 5C 0F / 70 10 7F 7F 04 00 00 2B / 08 0A 00 68 66 0F 20 01 / 3C 00 34 7E 7F 62 08 00 / 26 27 70 0F 65 7B 7F 14 / 13 02 00 29 09 00 5D 78 / 35 0F 26 41 05 64 59 7A / 04 00 00 00 61 50 1F 00 / 10 00 00 5D 4D 20 10 26 / 76 40 73 0C 1F 70 59 3F / 18 2F 25 60 1F 7D 20 73 / 23 79 40 2E 0E 1F 0D 06 / 0E 3F 33 74 60 08 27 21 / 7C 28 4C 42 6B 7A 1B 58 / 15 33 3D 0E 5D 62 64 55 / 08 21 45 68 46 2F 32 19 / 66 3B 17 39 6D 78 64 69 / 56 5C 27 46 18 4A 3F 41 / 17 12 3A 67 35 57 61 65 / 06 42 58 2C 12 36 54 48 / 51 77 09 6E 49 2B 75 30 / 47 69 00 00 20 44 28 7D / 00 00 00 00 3C 57 02 00 / 0A 00 00 29 73 0C 57 0C / 42 73 00 00 00 1B 0C 1F / 0C 00 00 00 5B 2D 22 6D / 2B 2C 44 31 23 19 13 53 / 3A 3B 73 2E 63 49 52 21 / 15 19 03 44 2B 68 1A 67 / 57 7C 3B 09 45 63 11 36 / 18 38 7D 18 6A 00 00 00 / 70 71 30 7C 00 00 00 00 / 44 16 02 26 0C 00 0C 0C / 01 0C 3C 3C 33 33 2F 19 / 5C 19 11 1A 19 71 00 00 / 40 60	01 02 00 3C 06 00 00 48 . . . < . . . H / 49 47 41 49 4E 00 02 4B I G A I N . . K / FE FF FF 1C 00 00 00 00 . . . . . . . . / 00 B2 13 F0 FF FF FF 16 . . . . . . . . / 00 00 33 00 00 CC 13 F0 . . 3 . . . . . / FE FF FF 10 00 00 59 00 . . . . . . Y . / 00 14 14 F0 FF FF FF 0A . . . . . . . . / 00 00 74 00 00 7C 14 F0 . . t . . | . . / FE FF FF 04 00 00 82 00 . . . . . . . . / 00 F8 14 F0 FE FF FF FE . . . . . . . . / FF FF 84 00 00 7D 15 F0 . . . . . } . . / FF FF FF F8 FF FF 7A 00 . . . . . . z . / 00 FE 15 F0 FE FF FF F3 . . . . . . . . / FF FF 64 00 00 6F 16 F0 . . d . . o . . / 00 00 00 EA FF FF 40 00 . . . . . . @ . / 00 C2 16 F0 F5 FF FF EC . . . . . . . . / FF FF 15 00 00 EC 16 F0 . . . . . . . . / 21 00 00 CA FF FF CB FF ! . . . . . . . / FF E3 16 F0 7B FF FF 2C . . . . { . . , / 00 00 C0 FF FF 97 16 F0 . . . . . . . . / E7 01 00 9D FE FF 89 FE . . . . . . . . / FF FE 15 F0 DB F8 FF 53 . . . . . . . S / 04 00 78 01 00 0B 15 F0 . . x . . . . . / A9 CD 02 E3 EE FF B0 F4 . . . . . . . . / FF B2 13 F0 C6 A7 FC DE . . . . . . . . / 57 08 6F 3B 08 ED C4 F2 W . o ; . . . . / 42 93 FE 2F 4F FE 7B E2 B . . / O . { . / 0E 00 00 00 1F D0 01 F5 . . . . . . . . / 08 FA 9E 3A 07 EC C4 0B . . . : . . . . / 1B 30 00 51 79 FF E3 BC . 0 . Q y . . . / 00 9D D8 0E 4F F5 FF A4 . . . . O . . . / 09 00 D8 3F 00 ED 3E 0F . . . ? . . > . / 44 05 00 92 E9 FF 0E 33 D . . . . . . 3 / 00 BA 7D 0F 3B 00 00 5F . . } . ; . . _ / F9 FF FD 15 00 9D 9F 0F . . . . . . . . / 68 04 00 12 FA FF 6D 09 h . . . . . m . / 00 34 AF 0F BF F8 FF 4A . 4 . . . . . J / 07 00 C9 0A 00 1B B7 0F . . . . . . . . / DC 08 00 86 F1 FF 99 03 . . . . . . . . / 00 ED C1 0F 26 FB FF 19 . . . . & . . . / 0C 00 38 01 00 E8 BF 0F . . 8 . . . . . / 30 01 00 8C FD FF DD 0A 0 . . . . . . . / 00 60 C8 0F 8C FF FF 1E . ` . . . . . . / 01 00 87 09 00 FA D1 0F . . . . . . . . / 16 00 00 C1 FF FF 66 0A . . . . . . f . / 00 2B DC 0F 90 FF FF 04 . + . . . . . . / 00 00 2B 0A 00 68 E6 0F . . + . . h . . / 20 01 00 B4 FE FF E2 08 . . . . . . . / 00 27 F0 0F 65 FB FF 14 . ' . . e . . . / 02 00 A9 09 00 DD F8 0F . . . . . . . . / A6 C1 05 E4 59 FA 00 00 . . . . Y . . . / 00 61 D0 1F 00 00 00 DD . a . . . . . . / 4D 20 10 26 C0 F3 8C 1F M . & . . . . / F0 D9 3F 2F 25 E0 9F 7D . . ? / % . . } / 20 73 79 C0 2E 0E 1F 8D s y . . . . . / 86 3F 33 74 E0 88 A7 21 . ? 3 t . . . ! / A8 CC C2 EB FA 1B 58 33 . . . . . . X 3 / 3D 8E 5D E2 64 D5 21 45 = . ] . d . ! E / 68 C6 2F 32 19 BB 97 39 h . / 2 . . . 9 / 6D F8 E4 69 DC 27 C6 18 m . . i . ' . . / CA BF 41 12 3A E7 35 D7 . . A . : . 5 . / E1 E5 42 58 2C 12 B6 D4 . . B X , . . . / 48 F7 09 EE 49 2B 75 B0 H . . . I + u . / E9 00 00 20 C4 A8 FD 00 . . . . . . . / 00 00 3C 57 02 00 00 00 . . < W . . . . / 29 F3 0C D7 0C F3 00 00 ) . . . . . . . / 00 1B 8C 1F 00 00 00 DB . . . . . . . . / AD 22 6D 2C C4 31 A3 19 . " m , . 1 . . / 93 D3 3B F3 AE E3 49 D2 . . ; . . . I . / 21 19 03 C4 2B E8 1A E7 ! . . . + . . . / FC 3B 89 45 E3 91 B6 38 . ; . E . . . 8 / 7D 98 EA 00 00 00 F1 B0 } . . . . . . . / FC 00 00 00 00 96 02 26 . . . . . . . & / 0C 80 0C 0C 0C 3C 3C 33 . . . . . < < 3 / 33 2F 99 99 11 9A 99 F1 3 / . . . . . . / 00 00 E0 . . .
Checksum	21
End of System Exclusive	F7

## Patch Dump Reply Message 3 (2A)
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	2A
Packed Data	00 01 02 00 3D 07 00 00 / 00 56 20 34 58 31 32 00 / 00 01 00 00 00 00 00 00 / 00 00 02 00 0C 00 18 00 / 05 38 00 6F 00 29 00 6D / 0A 00 41 01 0F 01 61 01 / 01 25 02 41 02 25 02 17 / 2D 01 14 00 4F 7F 51 7F / 39 5A 7F 7C 7F 49 00 1F / 0A 00 20 01 6C 00 12 00 / 47 11 00 32 00 6C 7F 6E / 7F 7F 37 7F 25 7F 66 7F / 7E 5B 7F 23 7F 25 7F 5C / 55 7F 15 7F 2E 7F 18 7F / 2A 10 7F 33 7F 17 7F 0A / 5F 7F 07 7F 76 7E 75 7E / 2B 20 7F 46 7F 57 7F 0E / 75 7F 0B 7F 5B 7F 29 7F / 7A 6B 7E 6F 7E 23 7F 40 / 5F 7F 71 7F 34 7F 4C 7F / 7F 40 7F 2C 7F 1C 7F 1A / 7F 7F 20 7F 0D 7F 12 7F / 7F 1F 7F 12 7F 0E 7F 20 / 7F 7F 28 7F 1A 7F 01 7F / 2F 7C 7F 7F 7F 10 7F 26 / 7C 7F 3B 7F 67 7F 03 00 / 00 0C 00 13 00 16 00 08 / 3C 00 76 7F 7E 7F 0A 00 / 07 11 00 12 00 7A 7F 55 / 7F 7F 2B 7F 10 7F 06 7F / 7F 0D 7F 22 7F 23 7F 33 / 7C 7F 60 7F 7B 7F 02 00 / 7F 7E 7F 77 7F 50 7F 31 / 7F 7F 36 7F 47 7F 68 7F / 00 0F 00 2C 00 43 00 4F / 00 00 4E 00 40 00 31 00 / 00 22 00 1F 00 2C 00 39 / 00 00 47 00 47 00 35 00 / 00 24 00 19 00 1A 00	01 02 00 3D 07 00 00 56 . . . = . . . V / 20 34 58 31 32 00 01 00 4 X 1 2 . . . / 00 00 00 00 00 00 02 00 . . . . . . . . / 0C 00 18 00 38 00 6F 00 . . . . 8 . o . / A9 00 ED 00 41 01 8F 01 . . . . A . . . / E1 01 25 02 41 02 25 02 . . % . A . % . / 97 01 94 00 CF FF 51 FF . . . . . . Q . / 5A FF FC FF 49 00 9F 00 Z . . . I . . . / 20 01 EC 00 92 00 91 00 . . . . . . . / 32 00 EC FF EE FF B7 FF 2 . . . . . . . / A5 FF E6 FF DB FF A3 FF . . . . . . . . / A5 FF 5C FF 15 FF 2E FF . . \ . . . . . / 18 FF 10 FF 33 FF 17 FF . . . . 3 . . . / 0A FF 07 FF F6 FE F5 FE . . . . . . . . / 20 FF 46 FF 57 FF 8E FF . F . W . . . / 8B FF 5B FF 29 FF EB FE . . [ . ) . . . / EF FE 23 FF 40 FF 71 FF . . # . @ . q . / B4 FF CC FF C0 FF AC FF . . . . . . . . / 9C FF 9A FF A0 FF 8D FF . . . . . . . . / 92 FF 9F FF 92 FF 8E FF . . . . . . . . / A0 FF A8 FF 9A FF 81 FF . . . . . . . . / 7C FF 7F FF 90 FF A6 FF | . . . . . . / BB FF E7 FF 03 00 0C 00 . . . . . . . . / 13 00 16 00 08 00 F6 FF . . . . . . . . / FE FF 0A 00 11 00 12 00 . . . . . . . . / FA FF D5 FF AB FF 90 FF . . . . . . . . / 86 FF 8D FF A2 FF A3 FF . . . . . . . . / B3 FF E0 FF FB FF 02 00 . . . . . . . . / FE FF F7 FF D0 FF B1 FF . . . . . . . . / B6 FF C7 FF E8 FF 0F 00 . . . . . . . . / 2C 00 43 00 4F 00 4E 00 , . C . O . N . / 40 00 31 00 22 00 1F 00 @ . 1 . " . . . / 2C 00 39 00 47 00 47 00 , . 9 . G . G . / 35 00 24 00 19 00 1A 00 5 . $ . . . . .
Checksum	55
End of System Exclusive	F7

## Patch Dump Reply Message 4 (2A)
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	2A
Packed Data	00 01 02 00 3C 08 00 00 / 00 48 49 47 41 49 4E 00 / 1C 02 4B 7E 7F 7F 1C 00 / 05 00 00 00 00 32 13 70 / 70 7F 7F 7F 16 00 00 33 / 17 00 00 4C 13 70 7E 7F / 40 7F 10 00 00 59 00 00 / 1E 14 14 70 7F 7F 7F 0A / 00 00 00 74 00 00 7C 14 / 78 70 7E 7F 7F 04 00 00 / 4B 02 00 00 78 14 70 7E / 7E 7F 7F 7E 7F 7F 04 00 / 0F 00 7D 15 70 7F 7F 7F / 71 78 7F 7F 7A 00 00 7E / 3F 15 70 7E 7F 7F 73 7F / 41 7F 64 00 00 6F 16 70 / 0E 00 00 00 6A 7F 7F 40 / 17 00 00 42 16 70 75 7F / 78 7F 6C 7F 7F 15 00 00 / 51 6C 16 70 21 00 00 4A / 7E 7F 7F 4B 7F 7F 63 16 / 58 70 7B 7F 7F 2C 00 00 / 7B 40 7F 7F 17 16 70 67 / 1F 01 00 1D 7E 7F 09 7E / 6F 7F 7E 15 70 5B 78 7F / 00 53 04 00 78 01 00 0B / 3B 15 70 29 4D 02 63 6E / 7D 7F 30 74 7F 32 13 70 / 78 46 27 7C 5E 57 08 6F / 1D 3B 08 6D 44 72 42 13 / 4A 7E 2F 4F 7E 7B 62 0E / 05 00 00 00 1F 50 01 75 / 33 08 7A 1E 3A 07 6C 44 / 01 0B 1B 30 00 51 79 7F / 6C 63 3C 00 1D 58 0E 4F / 72 75 7F 24 09 00 58 3F / 20 00 6D 3E 0F 44 05 00 / 71 12 69 7F 0E 33 00 3A / 01 7D 0F 3B 00 00 5F 79 / 66 7F 7D 15 00 1D 1F 0F / 06 68 04 00 12 7A 7F 6D / 0B 09 00 34 2F 0F 3F 78 / 44 7F 4A 07 00 49 0A 00 / 29 1B 37 0F 5C 08 00 06 / 73 71 7F 19 03 00 6D 41 / 18 0F 26 7B 7F 19 0C 00 / 0C 38 01 00 68 3F 0F 30 / 1E 01 00 0C 7D 7F 5D 0A / 17 00 60 48 0F 0C 7F 7F / 09 1E 01 00 07 09 00 7A / 43 51 0F 16 00 00 41 7F / 42 7F 66 0A 00 2B 5C 0F / 70 10 7F 7F 04 00 00 2B / 08 0A 00 68 66 0F 20 01 / 3C 00 34 7E 7F 62 08 00 / 26 27 70 0F 65 7B 7F 14 / 13 02 00 29 09 00 5D 78 / 35 0F 26 41 05 64 59 7A / 04 00 00 00 61 50 1F 00 / 10 00 00 5D 4D 20 10 26 / 76 40 73 0C 1F 70 59 3F / 18 2F 25 60 1F 7D 20 73 / 23 79 40 2E 0E 1F 0D 06 / 0E 3F 33 74 60 08 27 21 / 7C 28 4C 42 6B 7A 1B 58 / 15 33 3D 0E 5D 62 64 55 / 08 21 45 68 46 2F 32 19 / 66 3B 17 39 6D 78 64 69 / 56 5C 27 46 18 4A 3F 41 / 17 12 3A 67 35 57 61 65 / 06 42 58 2C 12 36 54 48 / 51 77 09 6E 49 2B 75 30 / 47 69 00 00 20 44 28 7D / 00 00 00 00 3C 57 02 00 / 0A 00 00 29 73 0C 57 0C / 42 73 00 00 00 1B 0C 1F / 0C 00 00 00 5B 2D 22 6D / 2B 2C 44 31 23 19 13 53 / 3A 3B 73 2E 63 49 52 21 / 15 19 03 44 2B 68 1A 67 / 57 7C 3B 09 45 63 11 36 / 18 38 7D 18 6A 00 00 00 / 70 71 30 7C 00 00 00 00 / 44 16 02 26 0C 00 0C 0C / 01 0C 3C 3C 33 33 2F 19 / 5C 19 11 1A 19 71 00 00 / 40 60	01 02 00 3C 08 00 00 48 . . . < . . . H / 49 47 41 49 4E 00 02 4B I G A I N . . K / FE FF FF 1C 00 00 00 00 . . . . . . . . / 00 B2 13 F0 FF FF FF 16 . . . . . . . . / 00 00 33 00 00 CC 13 F0 . . 3 . . . . . / FE FF FF 10 00 00 59 00 . . . . . . Y . / 00 14 14 F0 FF FF FF 0A . . . . . . . . / 00 00 74 00 00 7C 14 F0 . . t . . | . . / FE FF FF 04 00 00 82 00 . . . . . . . . / 00 F8 14 F0 FE FF FF FE . . . . . . . . / FF FF 84 00 00 7D 15 F0 . . . . . } . . / FF FF FF F8 FF FF 7A 00 . . . . . . z . / 00 FE 15 F0 FE FF FF F3 . . . . . . . . / FF FF 64 00 00 6F 16 F0 . . d . . o . . / 00 00 00 EA FF FF 40 00 . . . . . . @ . / 00 C2 16 F0 F5 FF FF EC . . . . . . . . / FF FF 15 00 00 EC 16 F0 . . . . . . . . / 21 00 00 CA FF FF CB FF ! . . . . . . . / FF E3 16 F0 7B FF FF 2C . . . . { . . , / 00 00 C0 FF FF 97 16 F0 . . . . . . . . / E7 01 00 9D FE FF 89 FE . . . . . . . . / FF FE 15 F0 DB F8 FF 53 . . . . . . . S / 04 00 78 01 00 0B 15 F0 . . x . . . . . / A9 CD 02 E3 EE FF B0 F4 . . . . . . . . / FF B2 13 F0 C6 A7 FC DE . . . . . . . . / 57 08 6F 3B 08 ED C4 F2 W . o ; . . . . / 42 93 FE 2F 4F FE 7B E2 B . . / O . { . / 0E 00 00 00 1F D0 01 F5 . . . . . . . . / 08 FA 9E 3A 07 EC C4 0B . . . : . . . . / 1B 30 00 51 79 FF E3 BC . 0 . Q y . . . / 00 9D D8 0E 4F F5 FF A4 . . . . O . . . / 09 00 D8 3F 00 ED 3E 0F . . . ? . . > . / 44 05 00 92 E9 FF 0E 33 D . . . . . . 3 / 00 BA 7D 0F 3B 00 00 5F . . } . ; . . _ / F9 FF FD 15 00 9D 9F 0F . . . . . . . . / 68 04 00 12 FA FF 6D 09 h . . . . . m . / 00 34 AF 0F BF F8 FF 4A . 4 . . . . . J / 07 00 C9 0A 00 1B B7 0F . . . . . . . . / DC 08 00 86 F1 FF 99 03 . . . . . . . . / 00 ED C1 0F 26 FB FF 19 . . . . & . . . / 0C 00 38 01 00 E8 BF 0F . . 8 . . . . . / 30 01 00 8C FD FF DD 0A 0 . . . . . . . / 00 60 C8 0F 8C FF FF 1E . ` . . . . . . / 01 00 87 09 00 FA D1 0F . . . . . . . . / 16 00 00 C1 FF FF 66 0A . . . . . . f . / 00 2B DC 0F 90 FF FF 04 . + . . . . . . / 00 00 2B 0A 00 68 E6 0F . . + . . h . . / 20 01 00 B4 FE FF E2 08 . . . . . . . / 00 27 F0 0F 65 FB FF 14 . ' . . e . . . / 02 00 A9 09 00 DD F8 0F . . . . . . . . / A6 C1 05 E4 59 FA 00 00 . . . . Y . . . / 00 61 D0 1F 00 00 00 DD . a . . . . . . / 4D 20 10 26 C0 F3 8C 1F M . & . . . . / F0 D9 3F 2F 25 E0 9F 7D . . ? / % . . } / 20 73 79 C0 2E 0E 1F 8D s y . . . . . / 86 3F 33 74 E0 88 A7 21 . ? 3 t . . . ! / A8 CC C2 EB FA 1B 58 33 . . . . . . X 3 / 3D 8E 5D E2 64 D5 21 45 = . ] . d . ! E / 68 C6 2F 32 19 BB 97 39 h . / 2 . . . 9 / 6D F8 E4 69 DC 27 C6 18 m . . i . ' . . / CA BF 41 12 3A E7 35 D7 . . A . : . 5 . / E1 E5 42 58 2C 12 B6 D4 . . B X , . . . / 48 F7 09 EE 49 2B 75 B0 H . . . I + u . / E9 00 00 20 C4 A8 FD 00 . . . . . . . / 00 00 3C 57 02 00 00 00 . . < W . . . . / 29 F3 0C D7 0C F3 00 00 ) . . . . . . . / 00 1B 8C 1F 00 00 00 DB . . . . . . . . / AD 22 6D 2C C4 31 A3 19 . " m , . 1 . . / 93 D3 3B F3 AE E3 49 D2 . . ; . . . I . / 21 19 03 C4 2B E8 1A E7 ! . . . + . . . / FC 3B 89 45 E3 91 B6 38 . ; . E . . . 8 / 7D 98 EA 00 00 00 F1 B0 } . . . . . . . / FC 00 00 00 00 96 02 26 . . . . . . . & / 0C 80 0C 0C 0C 3C 3C 33 . . . . . < < 3 / 33 2F 99 99 11 9A 99 F1 3 / . . . . . . / 00 00 E0 . . .
Checksum	42
End of System Exclusive	F7

## Patch Dump Reply Message 5 (2A)
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	2A
Packed Data	00 01 02 00 3D 09 00 00 / 00 56 20 34 58 31 32 00 / 00 01 00 00 00 00 00 00 / 00 00 02 00 0C 00 18 00 / 05 38 00 6F 00 29 00 6D / 0A 00 41 01 0F 01 61 01 / 01 25 02 41 02 25 02 17 / 2D 01 14 00 4F 7F 51 7F / 39 5A 7F 7C 7F 49 00 1F / 0A 00 20 01 6C 00 12 00 / 47 11 00 32 00 6C 7F 6E / 7F 7F 37 7F 25 7F 66 7F / 7E 5B 7F 23 7F 25 7F 5C / 55 7F 15 7F 2E 7F 18 7F / 2A 10 7F 33 7F 17 7F 0A / 5F 7F 07 7F 76 7E 75 7E / 2B 20 7F 46 7F 57 7F 0E / 75 7F 0B 7F 5B 7F 29 7F / 7A 6B 7E 6F 7E 23 7F 40 / 5F 7F 71 7F 34 7F 4C 7F / 7F 40 7F 2C 7F 1C 7F 1A / 7F 7F 20 7F 0D 7F 12 7F / 7F 1F 7F 12 7F 0E 7F 20 / 7F 7F 28 7F 1A 7F 01 7F / 2F 7C 7F 7F 7F 10 7F 26 / 7C 7F 3B 7F 67 7F 03 00 / 00 0C 00 13 00 16 00 08 / 3C 00 76 7F 7E 7F 0A 00 / 07 11 00 12 00 7A 7F 55 / 7F 7F 2B 7F 10 7F 06 7F / 7F 0D 7F 22 7F 23 7F 33 / 7C 7F 60 7F 7B 7F 02 00 / 7F 7E 7F 77 7F 50 7F 31 / 7F 7F 36 7F 47 7F 68 7F / 00 0F 00 2C 00 43 00 4F / 00 00 4E 00 40 00 31 00 / 00 22 00 1F 00 2C 00 39 / 00 00 47 00 47 00 35 00 / 00 24 00 19 00 1A 00	01 02 00 3D 09 00 00 56 . . . = . . . V / 20 34 58 31 32 00 01 00 4 X 1 2 . . . / 00 00 00 00 00 00 02 00 . . . . . . . . / 0C 00 18 00 38 00 6F 00 . . . . 8 . o . / A9 00 ED 00 41 01 8F 01 . . . . A . . . / E1 01 25 02 41 02 25 02 . . % . A . % . / 97 01 94 00 CF FF 51 FF . . . . . . Q . / 5A FF FC FF 49 00 9F 00 Z . . . I . . . / 20 01 EC 00 92 00 91 00 . . . . . . . / 32 00 EC FF EE FF B7 FF 2 . . . . . . . / A5 FF E6 FF DB FF A3 FF . . . . . . . . / A5 FF 5C FF 15 FF 2E FF . . \ . . . . . / 18 FF 10 FF 33 FF 17 FF . . . . 3 . . . / 0A FF 07 FF F6 FE F5 FE . . . . . . . . / 20 FF 46 FF 57 FF 8E FF . F . W . . . / 8B FF 5B FF 29 FF EB FE . . [ . ) . . . / EF FE 23 FF 40 FF 71 FF . . # . @ . q . / B4 FF CC FF C0 FF AC FF . . . . . . . . / 9C FF 9A FF A0 FF 8D FF . . . . . . . . / 92 FF 9F FF 92 FF 8E FF . . . . . . . . / A0 FF A8 FF 9A FF 81 FF . . . . . . . . / 7C FF 7F FF 90 FF A6 FF | . . . . . . / BB FF E7 FF 03 00 0C 00 . . . . . . . . / 13 00 16 00 08 00 F6 FF . . . . . . . . / FE FF 0A 00 11 00 12 00 . . . . . . . . / FA FF D5 FF AB FF 90 FF . . . . . . . . / 86 FF 8D FF A2 FF A3 FF . . . . . . . . / B3 FF E0 FF FB FF 02 00 . . . . . . . . / FE FF F7 FF D0 FF B1 FF . . . . . . . . / B6 FF C7 FF E8 FF 0F 00 . . . . . . . . / 2C 00 43 00 4F 00 4E 00 , . C . O . N . / 40 00 31 00 22 00 1F 00 @ . 1 . " . . . / 2C 00 39 00 47 00 47 00 , . 9 . G . G . / 35 00 24 00 19 00 1A 00 5 . $ . . . . .
Checksum	5B
End of System Exclusive	F7

## Patch Dump Reply Message 6 (26)
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	26
Packed Data	04 02 02 00 03 00 00 03 / 04 05 03 00 62 7F 00 00 / 22 00 7F 00 00 00 0A 02 / 08 00 00 01 7F 00 00 00 / 42 0B 02 00 00 01 7F 00 / 00 00 00	02 02 00 03 80 00 03 05 . . . . . . . . / 03 00 62 FF 00 00 00 FF . . b . . . . . / 00 00 00 8A 02 00 00 01 . . . . . . . . / FF 00 00 00 8B 02 00 00 . . . . . . . . / 01 FF 00 00 00 . . . . .
Checksum	6D
End of System Exclusive	F7

## Patch Dump Reply Message 7 (28)
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	26
Packed Data	00 01 02 00 10 00 00 00 / 00 01 50 01 01 01 00 00 / 00 51 02 01 01 01 00 52 / 00 03 01 01 02 00 53 04 / 00 01 01 03 00 28 05 00 / 00 00 3C 06 01 01 04 00 / 00 3D 07 01 01 06 00 3C / 00 08 01 01 04 00 3D 09 / 00 01 01 08 00 54 0A 01 / 00 01 07 00 55 0B 01 02 / 00 0A 00 56 0C 02 02 0B / 00 00 0B 01 57 0D 02 02 / 00 0C 00 0C 01 14 0E 00 / 00 00 02 0F 02 00 0D 00 / 00 0D 01	01 02 00 10 00 00 00 01 . . . . . . . . / 50 01 01 01 00 00 51 02 P . . . . . Q . / 01 01 01 00 52 03 01 01 . . . . R . . . / 02 00 53 04 01 01 03 00 . . S . . . . . / 28 05 00 00 3C 06 01 01 ( . . . < . . . / 04 00 3D 07 01 01 06 00 . . = . . . . . / 3C 08 01 01 04 00 3D 09 < . . . . . = . / 01 01 08 00 54 0A 01 01 . . . . T . . . / 07 00 55 0B 01 02 0A 00 . . U . . . . . / 56 0C 02 02 0B 00 0B 01 V . . . . . . . / 57 0D 02 02 0C 00 0C 01 W . . . . . . . / 14 0E 00 00 02 0F 02 00 . . . . . . . . / 0D 00 0D 01 . . . .
Checksum	41
End of System Exclusive	F7

## Patch Dump Reply Message 8 (22)
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	22
Packed Data	00 01
Checksum	65
End of System Exclusive	F7

End of patch dump

# Change Patch (2D)

System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	2D
Data	00 01 01 00 00	01: User, 00: Factory / 0-2F: Patch 1 - 128
Checksum	6B
End of System Exclusive	F7

## Response Acknowledge 7E
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	7E
Data	00 01 2D 00
Checksum	14
End of System Exclusive	F7

# Request Current Patch Name (20)
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	20
Data	00 01 01 00 1F
Checksum	79
End of System Exclusive	F7

## Response Data 21
System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	21
Packed Data	00 01 01 00 48 59 42 52 / 09 49 44 00 7F 08 09 29 / 00 00	01 01 00 48 59 42 52 49 . . . H Y B R I / 44 00 FF 08 09 A9 00 D . . . . . .
Checksum	36
End of System Exclusive	F7

# Message (2E): Patch name changed

Sent after patch saved

System Exclusive	F0
Manufacturer ID	00 00 10
MIDI Channel	00
Device ID	56
Command Code	2E
Data	00 01 00
Bank	BB	01: User, 00: Factory
Patch	PP	0-2F: Patch 0 – 2F (1 - 48)
Patch Name	Null terminated string
Checksum	XX
End of System Exclusive	F7

240, 0, 0, 16, 0, 86, 46, 0, 1, 0, 1, 0, 72, 89, 66, 0, 82, 73, 68, 0, 0, 100, 247 # patch 1
240, 0, 0, 16, 0, 86, 46, 0, 1, 0, 1, 1, 73, 89, 66, 0, 82, 73, 68, 0, 0, 100, 247 # patch 2
240, 0, 0, 16, 0, 86, 46, 0, 1, 0, 1, 2, 74, 89, 66, 0, 82, 73, 68, 0, 0, 100, 247 # patch 3